## Slide 1: Gaussian-process-augmented projection-based model order reduction
Carlos González Hernández, Radek Tezaur, Charbel Farhat
Stanford University
APS DFD 2024

## Slide 2: Motivation
  Many important engineering applications rely on many queries of high-dimensional computational models
    Model predictive control
    Uncertainty quantification
    Design analysis & optimization
  Surrogate models are often required for these to be computationally tractable
    Seek a more parsimonious description of the high-dimensional model through dimensionality reduction
  Dimensionality reduction approaches
    External representations: linear regression, gaussian process regression, artificial neural network regression
    Internal representations: operator-inference model, physics-informed neural networks, projection-based reduced-order models

## Slide 3: Projection-based model order reduction (PMOR)
  Principled, physics-based method for machine learning with model(s) and data
  Semi-discrete or discrete, parametric, linear or nonlinear computational model
  , , , , very large, moderately large
  Hypothesis: best approximation of the solution in a lower-dimensional space
  e.g. (traditional PROM)
  Representation: reduced-order basis (ROB)
  Data-driven learning: ROB is learned from solutions snapshots and their compression
  Minimization of a loss function

## Slide 4: Challenge in PMOR – breaking the Kolmogorov n-width
  PMOR based on the affine subspace approximation , where
  , ,
  For convection-dominated PDEs, the convergence of a subspace approximation is limited by the slow decay of the Kolmogorov -width
  Recent strategies for mitigating this issue share the abandonment of the traditional affine approximation in favour of a nonlinear one (nonlinear PMOR): piecewise linear approximation; autoencoder-based approximation; nonlinear parametrization of affine approximation; quadratic approximation manifold
  For most linear problems, exhibits exponential decay; for convection-dominated flow problems, it exhibits a decay of

## Slide 5: Arbitrarily nonlinear approx. for mitigating Kolmogorov barrier
  Nonlinear approximation manifold generated by a ROB and an ANN:
    using the first columns of , where (PROM)
    using a subset of the next columns of
    is a map represented by an ANN
    Projection of solution onto ,
  Objectives
    Demonstrated on inviscid Burgers’ problem and double cone hypersonic flow benchmark problem
  Challenges
    Can’t derive mathematical bounds for errors (i.e. black box)
  Construction of a ROB for: a traditional PROM (left); and a PROM-ANN (right)
PROM-ANN (Barnett et al. 2023, JCP)

## Slide 6: Application: Inviscid Burgers’ problem
  Computational domain:
  Time interval:
  Parameter domain: , uniform sampling by a 3 x 3 grid  9 training parameter points characterized by and
  Computing system: 1 node with 24 cores, CPU: 2.3GHz, RAM (shared): 192 GB
  4,501 solutions snapshots
  Godunov-type scheme on two uniform meshes:
  M1: , M2:
  Trapezoidal method and constant ( time-steps)
  (in all cases)
  2-norm based relative error

## Slide 7: Application: Inviscid Burgers’ problem

## Slide 8: Alternative approach for building the map in the latent space: gaussian process
  Original ANN: 4 layers (Barnett et al. 2023, JCP)
  Test with 1 layer: relative errors of 1.5% vs 0.8%
  Deep learning is therefore *not needed*  replace ANN by GP regression which is analyzable
  A GP is a collection of random variables, any finite number of which have Gaussian distributions
  A GP is fully specified by a mean function and covariance function
  The stochasticity might be used for uncertainty quantification; beyond scope of this talk
  Our problem: ,
  scikit-learn for constructing the map and its gradient
  All tests are performed on out-of-sample values, reported only most unfavorable case

## Slide 9: M1,
RE= 1.51%
RE= 3.44%
Numerical predictions performed using the LSPG- and
ECSW-based HPROM-ANN with ,
Numerical predictions performed using the LSPG- and
ECSW-based HPROM-GP with ,

## Slide 10: M2,
RE=3.42%
RE=4.68%
Numerical predictions performed using the LSPG- and
ECSW-based HPROM-ANN with ,
Numerical predictions performed using the LSPG- and
ECSW-based HPROM-GP with ,

## Slide 11: Offline performance (wall clock time)
Computational Model (offline) | n (N for HDM) | for HDM) | Time (minutes)
HDM | 125,000 | 62,500 | 106.92
PROM | 95 | 4,390 | 85.16
PROM-ANN | 10 | 1,496 | 22.24
PROM-GP | 10 | 1,496 | 17.53
HDM | 1,125,000 | 562,500 | 404.88
PROM | 95 | 63,106 | 45.25*
PROM-ANN | 10 | 3,496 | 24.54
PROM-GP | 10 | 3,496 | 24.25
Computational Model (offline) | n (N for HDM) |  | Time (minutes)
HDM | 125,000 | 62,500 | 106.92
PROM | 95 | 4,390 | 85.16
PROM-ANN | 10 | 1,496 | 22.24
PROM-GP | 10 | 1,496 | 17.53
HDM | 1,125,000 | 562,500 | 404.88
PROM | 95 | 63,106 | 45.25*
PROM-ANN | 10 | 3,496 | 24.54
PROM-GP | 10 | 3,496 | 24.25
Table: Model parameters and offline performance results for both meshes
*Domain decomposition was used for M2
Mesh
M1
Mesh
M2

## Slide 12: Online performance (wall clock time)
Table: Model parameters and online performance results for both meshes
Computational Model (online) | n (N for HDM) | for HDM) |  | Time (minutes) | Speedup factor
HDM | 125,000 | 62,500 | — | 106.92 | —
PROM | 95 | 4,390 | 1.43% | 1.11 | 96.3
PROM-ANN | 10 | 1,496 | 1.51% | 0.30 | 356.4
PROM-GP | 10 | 1,496 | 3.44% | 0.72 | 148.5
HDM | 1,125,000 | 562,500 | — | 404.88 | —
PROM | 95 | 63,106 | 7.98% | 35.79 | 11.31
PROM-ANN | 10 | 3,496 | 3.45% | 0.70 | 578.4
PROM-GP | 10 | 3,496 | 4.68% | 1.72 | 235.4
Computational Model (online) | n (N for HDM) |  |  | Time (minutes) | Speedup factor
HDM | 125,000 | 62,500 | — | 106.92 | —
PROM | 95 | 4,390 | 1.43% | 1.11 | 96.3
PROM-ANN | 10 | 1,496 | 1.51% | 0.30 | 356.4
PROM-GP | 10 | 1,496 | 3.44% | 0.72 | 148.5
HDM | 1,125,000 | 562,500 | — | 404.88 | —
PROM | 95 | 63,106 | 7.98% | 35.79 | 11.31
PROM-ANN | 10 | 3,496 | 3.45% | 0.70 | 578.4
PROM-GP | 10 | 3,496 | 4.68% | 1.72 | 235.4
Mesh
M1
Mesh
M2

## Slide 13: Conclusion & Future work
  Proposed concept of a PROM-GP approach based on the arbitrarily nonlinear approximation
  , , , ,
  GP’s training is performed in the latent space and thus does not involve data whose dimension scales with
  PROM-GP is hyperreducible using any well-established hyperreduction method
  For a parametric, 2D, inviscid Burgers’ problem, PROM-GP delivers the same desired
  level of accuracy as the traditional PROM
  The online phase of PROM-GP gives a similar level of accuracy as PROM-ANN, in a time ranging from same to double, although it is implementation-specific
  Main objective: deriving mathematical error bounds; future: showcase on CFD benchmark

## Slide 14: Back-up slides

## Slide 15: Hyperreduction using ECSW
  Reduced mesh M1: elements (2.4% of elements)
  Reduced mesh M2: elements (5.6% of elements)
  ECSW training:
    at only one of the sample parameter points – namely, (4.25, 0.0225)
    at every 10-th solution snapshot

## Slide 16: M1,
RE= 1.01%
RE= 2.08%
Numerical predictions performed using the LSPG- and
ECSW-based HPROM-ANN with ,
Numerical predictions performed using the LSPG- and
ECSW-based HPROM-GP with ,

## Slide 17: M1,
RE= 1.21%
RE= 1.62%
Numerical predictions performed using the LSPG- and
ECSW-based HPROM-ANN with ,
Numerical predictions performed using the LSPG- and
ECSW-based HPROM-GP with ,

## Slide 18: M2,
RE=3.45%
RE=4.10%
Numerical predictions performed using the LSPG- and
ECSW-based HPROM-ANN with ,
Numerical predictions performed using the LSPG- and
ECSW-based HPROM-GP with ,

## Slide 19: M2,
RE=3.28%
RE=4.47%
Numerical predictions performed using the LSPG- and
ECSW-based HPROM-ANN with ,
Numerical predictions performed using the LSPG- and
ECSW-based HPROM-GP with ,

## Slide 20: Alternative approach: gaussian processes
  Original ANN: 6 layers (4 hidden layers)
  Test with 1 hidden layer and various sizes
  We propose to replace ANN by a GP
  A GP is a collection of random variables, any finite number of which have Gaussian distributions
  A GP is fully specified by a mean function and covariance function
  Our problem: ,
  Matérn kernel:
ANN Type | Elapsed Time (s) | RE
4HL, original | 16.01 | 0.79%
1HL,(32,64) | 15.63 | 8.38%
1HL,(256,256) | 19.65 | 2.19%
1HL,(512,512) | 20.19 | 1.55%
1HL,(512,1024) | 22.80 | 1.74%
  (q,512) (512,1024) (1024,)
  ELU ELU
Barnett et al. 2023, JCP
  scikit-learn for constructing the map and its gradient
  All tests are performed on out-of-sample values